## Slide 1: 4-12-2025 Enclosure Design Updates

## Slide 2: List of Items to Update
Round all the edges
Add tolerance to the back door (shrink by 1 mm in x and 1 mm in y)
Reduce tolerance on screen fitting by 1 mm in x and 1 mm in y
Make screen mount inner sketch smaller
Align things properly in the assembly
Speaker mount hole spacing needs to be wider
Add a microphone mount

## Slide 3: Screen Mount Resizing
Increase right side overhang by 5 mm
Increase left side overhang by up to 15 mm
Increase down by 15 mm from top
Increase up by 20 mm from bottom
15 by 15 mm

## Slide 4: Speaker mount resizing
39.53 mm maximum distance between screw hole outer edges
currently, with oversized m3 screws (want #4 screws), the maximum distance between screw outer edges is 39.08 mm
loosely measuring, 39.67 mm vs 39.14 mm
so, regardless, want to make holes about 0.5 mm wider
okay, increased center-to-center from 36.5 to 37 mm
speaker holes 34.2 mm min. edge to edge
33.86 screws min edge to edge; still about 0.5 mm
but eyeballing things it looks like you need another 1 mm
just make both

## Slide 5: Microphone Mount
lower by 1.25 cm
36.5 mm – 12.5 mm = 24 mm
make a 2nd version with the center to center screw hole distance higher at 26.5 mm